## Slide 1: Subsurface Enhancement through Sparse Representations of Multispectral Direct/Global Decomposition
Achuta Kadambi, Hayato Ikoma,
Xing Lin, Gordon Wetzstein, Ramesh Raskar
Camera Culture Group

## Slide 2: Importance of Subskin Imaging
Vending Machine Authenticates your purchase and targets advertisements
Hitachi Presented 2009.
*This technique uses transmission imaging. In context of skin, reflectance is more challenging.

## Slide 3: Importance of Subskin Imaging
 | Iris | Voice | Face | FingerPrints | Vein
Ease of Use |  |  |  |  | 
Cheap |  |  |  |  | 
Accurate |  |  |  |  | 
Secure |  |  |  |  | 
Vein is more secure than Fingerprints (hard to alter your vein pattern unless through surgery).
Cheap and Easy to Use compared with Iris Detection. Table from Strickland, IEEE Spectrum 2012.

## Slide 4: Vein-Viewing: Spectral Profile of Hb and HbO2
Isobestic Point: 810nm

## Slide 5: Multispectral Subskin Imaging
VeinViewer is limited as an imaging technique.
Computational aspect is basically multispectral imaging (two wavelengths) and contrast enhancement.
VeinViewer ™ Clinical Device
VeinViewer ™ Projects an overlay pattern to guide IV needles.
Several companies now use this technology (e.g. Accuvein).
Clinical feedback is mixed but represents win for Augmented Reality Community.
How to add Computation to the Loop?

## Slide 6: Direct and Global Separation
[Nayar, Krishnan, Grossberg, Raskar SIGGRAPH 2006]
Direct Illumination is a low frequency phenomena
Global Illumination is high Frequency phenomena.
Separation is straightforward: High frequency coded illumination and image subtraction.
Notes: Relationship to Multipath

## Slide 7: Our approach – Skin “Phantom”
Our computational approach combines multispectral with high-frequency coded illumination.to perform multispectral global and direct separation.
Notes: Trace amounts of milk+cola.

## Slide 8: Conventional Multispectral Photography
430 nm
510 nm
700 nm
850 nm

## Slide 9
430 nm
510 nm
700 nm
850 nm
430 nm
510 nm
700 nm
850 nm
Direct/Surface Illumination
Global/Subsurface Illumination

## Slide 10: Multispectral versus Multispectral Global-Direct
Multispectral
Multispectral
Global Direct

## Slide 11: Applying the Technique
Veins are bright in the target image.

## Slide 12: Characterizing Direct and Global Light Transport
Direct Component
Global Component
Indirect Component
x
Additive Decomposition
Light Source
Camera

## Slide 13: Relationship between Global/Direct Transport and Subsurface Diffuser Imaging
x
Direct Component
Global Component
Diffuser
Subsurface
Pattern
Light Source
Camera

## Slide 14: Ambiguities in Global Transport
x
Attenuation
Factor:
Light
Source
Diffuser
Subsurface
Pattern
Different Light paths contribute to global illumination.

## Slide 15: Blurring in the Global Image
x
Global Image: Blurred Version of Subsurface
Direct Image: Image of the Surface
Conventional Photograph = Direct+Global
Diffuser
Subsurface
Pattern

## Slide 16: Frequency and Light Transport
Direct Illumination
Global
Illumination

## Slide 17: Frequency and Light Transport
Direct Illumination
Global
Illumination
Take-Home:
Global Illumination  Low Spatial Frequency Phenomena.
Direct Illumination  High Spatial Frequency Phenomenon.

## Slide 18: Combining Multispectral Global-Direct
Combination of multispectral global-direct is achieved by changing the wavelength of illumination (projector)
Optoma PK102 replaced with OSRAM SFH4232 850 nm
Acquired Dataset is a 4-hypercube
  Intensity in
  represents global or direct intensities.
Notes: This paper is an applications paper. Therefore we consider multispectral global direct.

## Slide 19: Simple Implementation
Notes: Simple Implementation

## Slide 20: Visual Roadmap

## Slide 21
Target Decomposition via Sparsity (Part II)
Multispectral Global/Direct (Part I)
Computer
Graphics/Vision
Computational Photography
Conventional Imaging
Photograph
Global
Spectral
Global
Target
Not Target
Direct
Spectral
Direct

## Slide 22: Sparse Coding
4-hypercube of Multispectral Direct and Global
Inputs
Outputs
Target Image and Not-Target Image: “Segmentation”

## Slide 23: Decomposing Global Light Transport

## Slide 24: Promoting Sparsity for
Convex Relaxation
Classifying the Coefficient Vector

## Slide 25: Forward Models of Spectral and Global Illumination in Graphics
[Tsumura et al. SIGGRAPH 2003]
[Donner et al. EGSR 2006]
By incorporating hemoglobin and melanin information, Tsumura et al. is able to change the skin color of a 50 year old woman to a 20 year old.
Top row: Increasing amounts of Hemoglobin under the skin for rendering.
Bottom row: Increasing amounts of Melanin.
At left, a plausible human face rendering by using Subsurface Scattering.
[Jimenez et al.
SIGGRAPH Asia 2010

## Slide 26: Inverse Problem of Imaging
How can we decompose this image into subsurface targets?

## Slide 27: Combined Image Acquisition

## Slide 28: Applying the Technique
Veins are the target

## Slide 29: Differences between Direct and Global for Skin
Direct
Global
430 nm
510 nm
700 nm
850 nm

## Slide 30: Decomposition into Target and Complement

## Slide 31: Segmentation/Contrast Enhancement

## Slide 32: Scope
Acquisition is not “real-time”.
  Limiting factor can be overcome in hardware  Motivates industry approach.
This talk assumes planar through diffuser techniques and does not perform descattering.
Rank of Dictionary is by no means limited to vein and not vein.
Sparsity not fully explored in the context of 4D acquisition. Number of measurements increases by square root of N, which opens up possibilities for Compressive framework.

## Slide 33: Looking Ahead
Achuta Kadambi: achoo@mit.edu
Discriminating photons via wavelength AND path properties encourages new computational applications.
Optical and Computational Co-design.
Technique is simple enough for industry transfer for subsurface imaging contexts.
Combining in context of Time Domain or Phase Imaging.
Additional Links:
Camera Culture Group, Mass. Inst Tech.
http://cameraculture.info
- If interested, opportunities in imaging for incoming graduate students who are thinking about applying to MIT. Also slots for postdoctoral researchers.

## Slide 39: Selective Targeting

## Slide 41: Simulating the Forward Model
Subsurface Pattern represents Albedo. Indirect Image represents measurements. Albedo and Intensity image are not on necessarily equivalent scales.

## Slide 42
[Chen et al. Bioinformatics and Biomedical Engineering (ICBBE) 2007]

## Slide 46
source
surface
P
Direct and Global Illumination
A
A : Direct
B
B : Interrelection
C
C : Subsurface
D
participating
medium
D : Volumetric
translucent
surface
E
E : Diffusion
camera

## Slide 47
direct
global
radiance
Direct and Global Components: Interreflections
surface
i
camera
source
j
BRDF and geometry

## Slide 48
Other Global Effects: Subsurface Scattering
translucent
surface
camera
source
i
j

## Slide 49
Other Global Effects: Volumetric Scattering
surface
camera
source
participating medium
i
j

## Slide 50
High Frequency Illumination Pattern
surface
camera
source
fraction of activated source elements
+
i
[Nayar, Krishnan, Grossberg, Raskar SIGGRAPH 2006]

## Slide 51
High Frequency Illumination Pattern
surface
fraction of activated source elements
camera
source
+
-
i
[Nayar, Krishnan, Grossberg, Raskar SIGGRAPH 2006]

## Slide 52
Separation from Two Images
direct
global
[Nayar, Krishnan, Grossberg, Raskar SIGGRAPH 2006]

## Slide 53: Forward Model of Light Transport

## Slide 54: Plugs
CS-MUVI Kevin Kelly.
  E.g. 4D dataset and sparsity. Fourth root.

## Slide 55: Blurring

## Slide 56: Frequency and Light Transport
Direct Illumination
Global
Illumination